## Slide 1
Multi-kilometre and
Multi-gigabit-per-second
Sub-THz Communications for Wireless Backhaul Applications
Presented By
Sai Anirudh Godavarthi Terahertz in 6G & Beyond – Spring 2026

## Slide 2
Agenda
Background
Problem Statement
Objectives
Methods
Experimental Setup
Results & Discussion
Limitations
Conclusion
Importance for 6G
Advantages

## Slide 3
Background: High Power Trans-receivers
6G and beyond require extremely high data rates.
Sub-terahertz band (100 GHz to 1 THz) offers large bandwidth.

## Slide 4: Background: Epitaxial structure of the receiver mixer.
Transmitter and receiver performance at 210–240 GHz
Long-distance wireless links at these frequencies are challenging.

## Slide 5
Limitations
Precise alignment required.
Atmospheric loss increases with frequency.
Hardware complexity still high.
Further optimization needed for tens of km links.

## Slide 6
Objectives

## Slide 7
Experimental Setup
Outdoor transmitter and receiver separated by 2.03 km.
Directional High-Gain Horn-lens antennas with 40 dBi / 55 dBi gain.
Receiver uses low-noise amplifier: 35 dB gain, 1 dB noise figure.
Signals transmitted around 225 GHz.

## Slide 8
Problem Statement
Methods: Power Combining & Signal Processing

## Slide 9
Methods: Transceiver Configurations
Full configuration of the transceiver chain with mixers, multipliers and amplifiers
with the corresponding powers at different stages.

## Slide 10
Results & Discussion
Data transmission using source-modulated (upconverter 1) and
IF-modulated (upconverter 2) system.

## Slide 11
Importance for 6G
Useful for wireless backhaul in cities and rural areas.
Fast emergency deployment when fiber is unavailable.
Can connect mmWave / Wi-Fi access points to core network.

## Slide 12
Advantages
High capacity without laying fiber.
Rapid deployment.
Scalable for future dense networks.
Potential lower infrastructure cost.

## Slide 13
Conclusion
This paper demonstrates that long-distance, high-speed sub-THz communication is practical and can play a major role in future 6G wireless backhaul systems.

## Slide 14
Thank You
Any Clarifications?